## Slide 1: Robot programming
Exercise 2

## Slide 2: Question 1 - Movement patterns
RobotConfigs contains information about our robot
Two methods of movement -
Direct motor control
Differential pilot
Improvements -
- Register the button press as an event
import lejos.nxt.Button;
import lejos.robotics.RegulatedMotor;
import lejos.robotics.navigation.DifferentialPilot;
public class Part1 {
public static void main(String[] args) {
RegulatedMotor rightMotor = RobotConfigs.getRightmotor();
RegulatedMotor leftMotor = RobotConfigs.getLeftmotor();
double wheelDiameter = RobotConfigs.getWheelDiameter();
double trackWidth = RobotConfigs.getTrackWidth();
DifferentialPilot pilot = new DifferentialPilot(wheelDiameter,
trackWidth, leftMotor, rightMotor, false);
System.out.println("Hello world!");
Button.waitForAnyPress();
leftMotor.backward();
rightMotor.forward();
Button.waitForAnyPress();
leftMotor.stop();
rightMotor.stop();
while (true) {
pilot.travel(300);
pilot.rotate(90);
}
}
}

## Slide 3: Question 2a - Bump and turn
import lejos.nxt.Button;
import lejos.nxt.SensorPort;
import lejos.nxt.TouchSensor;
import lejos.robotics.RegulatedMotor;
import lejos.robotics.navigation.DifferentialPilot;
public class Part2a {
public static void main(String[] args) {
RegulatedMotor rightMotor = RobotConfigs.getRightmotor();
RegulatedMotor leftMotor = RobotConfigs.getLeftmotor();
double wheelDiameter = RobotConfigs.getWheelDiameter();
double trackWidth = RobotConfigs.getTrackWidth();
DifferentialPilot pilot = new DifferentialPilot(wheelDiameter,
trackWidth, leftMotor, rightMotor, false);
TouchSensor t1 = new TouchSensor(SensorPort.S1);
TouchSensor t2 = new TouchSensor(SensorPort.S4);
Button.waitForAnyPress();
while (true) {
pilot.forward();
if (t1.isPressed() || t2.isPressed()) {
pilot.travel(-100);
pilot.arc(0, 180);
}
}
}
}
This implementation uses a while loop to detect the touch sensor being pressed
If either sensor gets pressed, the robot turns around and drives forward
We reused our RobotConfigs class

## Slide 4: Question 2b - Bump and turn
public class Part2b {
private final static DifferentialPilot pilot = RobotConfigs.getPilot();
public static void main(String[] args) {
SensorPortListener sensor = new Listener(pilot);
SensorPort.S1.addSensorPortListener(sensor);
SensorPort.S4.addSensorPortListener(sensor);
Button.waitForAnyPress();
pilot.forward();
Button.waitForAnyPress();
}
}
public class Listener implements SensorPortListener {
private DifferentialPilot pilot;
public Listener(DifferentialPilot pilot) {
this.pilot = pilot;
}
@Override
public void stateChanged(SensorPort aSource, int aOldValue, int aNewValue) {
if (aNewValue < 500) {
pilot.travel(-100);
pilot.arc(0, 180);
pilot.forward();
}
}
}
Event driven code structure
Two separate classes -
Main method class
Event handler
Difficulties -
Anonymous listeners failing, worked out for the best
Harder to code, but better overall

## Slide 5: Question 3 - Escape
uSensor.continuous();
while (true) {
pilot.forward();
System.out.println(uSensor.getDistance());
if (uSensor.getDistance() > 75) {
pilot.arc(10, 30);
pilot.travel(120);
}
if (uSensor.getDistance() < 15) {
pilot.arc(-8, -20);
while (uSensor.getDistance() < 5
|| uSensor.getDistance() == 255) {
pilot.travel(-50);
}
}
if (t1.isPressed()) {
pilot.travel(-75);
pilot.arc(0, 52);
}
if (t2.isPressed()) {
pilot.travel(-75);
pilot.arc(0, -52);
}
if (t1.isPressed() || t2.isPressed() && uSensor.getDistance() < 7) {
pilot.arc(0, 180);
pilot.travel(120);
pilot.arc(0, 60);
}
}
}
}
Our movements and sensor threshold were tweaked a lot throughout development
Ultrasonic sensors were easier to use than we thought
We used the direct approach, rather than using event handlers
Issues -
Only having one ultrasonic sensor